## Slide 1: Lidar Pose Estimator – Pipeline walkthrough
Presented by:
Hazem Mohsen Abdelaziz

## Slide 2: ROS2 Package
This package solves one problem: estimate the 6-DOF pose of a moving LiDAR sensor over time, using only the point cloud stream — no GPS, no IMU fusion,no wheel odometry.
It builds a map as it goes, and it ships a second node whose only job is to grade how accurate that estimate is against an external ground-truth source.
Two executables ship in this package:
1- lidar_pose_estimator_node
does the actual SLAM-style odometry
2-evaluation_node
compares it to ground truth and logs results

## Slide 3: Point cloud registration (NDT)
Why Normal Distributed Transform?
Models a point cloud as a grid of local Gaussian distributions, not raw points
Registration = find the rigid transform that best aligns a new scan's points against those distributions
Smooth, differentiable cost surface — better convergence behavior than raw ICP on noisy outdoor data

## Slide 4: High level data flow

## Slide 5: Per-frame pipeline
1. Convert ROS message → PCL point cloud
2. Voxel-downsampling
3. Range filter (remove too-near / too-far points)
4. Hard cap on point count (random subsample)
5. Bootstrap check — first frame seeds the map
6. Build initial guess from constant-velocity motion prior
7. NDT registration (scan-to-map, falls back to scan-to-scan)
8. Accept or reject based on fitness score
9. Accumulate accepted scan into the map
10. Publish odometry / pose / TF / path, log TUM line
11. Periodically publish the full map cloud
12- Converting to XYZ PCL to continue cycle processing

## Slide 6: Range filtering
Without it, an outdoor scan with well over 100,000 points produces NDT normal distributions so smooth that the identity transform looks like a valid optimum — the estimated pose simply doesn't move. Cutting points below the minimum range removes self-noise and reflections off the platform; cutting points beyond the maximum range removes far-field returns that flatten the gradient.
The side effect is also a big point-count reduction, typically down to five-to-fifteen thousand points, which keeps registration fast.

## Slide 7: BOOTSTRAP
First scan is treated as ground truth at identity
T_map_lidar_ and T_delta_ both initialized to identity
That first filtered scan is added directly to the map
Pose/odom/TF/path are published immediately, so downstream consumers see frame 0 with zero delay

## Slide 8: Const velocity estimates (Motion Prior)
The system predicts the next pose using the previous motion:
  Uses last two accepted poses to compute relative motion (T_delta)
  Extrapolates current initial guess: Tguess = Tmap_lidar * T_delta
Scan-to-map Vs Scan-to-Scan
Two registration modes depending on map size
  Early stage: scan-to-scan (frame-to-frame)
  Later stage: scan-to-map (full accumulated map)
Fallback exists if scan-to-map fails (relaxed retry on previous frame)

## Slide 9: Robust pose update & failure handling
NDT output is validated before being accepted
Conditions:
  Converged
  Fitness < threshold
If valid:
  Update pose (T_map_lidar)
  Update motion prior (T_delta)
If invalid:
  Keep last good pose
  Do NOT update motion model
  Track failure count

## Slide 10: Map construction strategy
Full filtered scan is transformed into map frame
Added to global accumulated map
NOT limited to NDT correspondence points → preserves structure
Periodic voxel re-filtering prevents memory explosion
Map published every N frames, not every scan

## Slide 11: System outputs and evaluation node purpose
Real-time outputs:
  /lidar_odom, /lidar_pose, /lidar_path
  TF: map → lidar
  /map_cloud (periodic)
Offline outputs:
  .pcd → final map
  .tum → trajectory
  .csv → logs (if evaluation used)
  Why Evaluation node?
Separate node for independent evaluation
Compares LiDAR odometry vs ground truth (ENU)
Computes error metrics without affecting SLAM
Fully decoupled from estimator

## Slide 12: Frame Alignment Problem & Solution
Problem:
  LiDAR frame = arbitrary origin + heading
  ENU frame = global reference (North-aligned)
Solution:
  Auto alignment using first pose yaw difference
  OR manual yaw offset override
Application:
  Fixed transform T_enu_to_map
  Applied to all ENU points

## Slide 13: Visualization and takeaway
RViz2 visualization:
  LiDAR path
  Ground truth ENU path
  Point cloud map
  Live error signal
Key system ideas:
  Heavy preprocessing → stable NDT
  Motion prior improves convergence
  Scan-to-map + fallback ensures robustness
  Bad frames are rejected, not propagated
  Fully reproducible evaluation pipeline